## Slide 1: Face Recognition Door Lock System with RISC-V
Paulo Fidalgo
Wagner Pedrosa

## Slide 2: Context
CTM Summer Internships at OET (Optic Electronics Technology) center
Integration of hardware and software in IoT (Internet of Things) applications
ESP32-CAM with RISC-V
Real-time face recognition

## Slide 3: Objectives
Design and build a door lock system using the ESP32-CAM
Apply face recognition software to enable secure access control
Develop a user-friendly interface for the system to allow easy management
Conduct testing and debugging to ensure the system is reliable and secure
Document the development process to facilitate future modifications
Provide guidelines for installation, operation and maintenance of the system

## Slide 4: Developed Work - Circuit

## Slide 5: Developed Work - Algorithm Pipeline

## Slide 6: Developed Work - Mobile App

## Slide 7: Results - Face Recognition Error
Training: 10 Genuine enrolled with 10 samples each
Test:
  20 Identities (10 genuine and 10 impostors)
  Same distance from camera, lighting conditions and background
  Randomly presented a person to the camera and got the corresponding similarity value
  Three times for each person
Results:
  Close distributions
  Cases of False Negative
  No False Positive
  Genuine:
    Maximum: 0.88
    Minimum: 0.45
  Impostor:
    Maximum: 0.45
    Minimum: 0.20

## Slide 8: Results - Energy Consumption
Results:
  Constant tension in ESP circuit: 5.17V
  Constant current for each task
  The image takes approximately 8s to be processed
  Door lock circuit consumption: 6W for 5s when opened
  Wi-Fi has a significant impact on power
Test:
  A multimeter was used to measure current and tension of both 5V and 12V circuits
  Each value was calculated using the “Power Equation” P (W) = V (V) * I (A)

## Slide 9: Conclusions